Police High Intensity Lighting & Flashing Device  OR-GXM90

Key technical parameters:

- Light source: LED   color temperature: 5700K-6000K

- One-button switch: Microswitch trigger, work mode: Weak light--Strong light--blasting flash 1-blasting flash 2-blasting flash 3-turn off, complete the switch among the functions by one hand.

- Maximum power: 9*10W, LED use constant current control, the brightness of light source is constant, and no brightness changeable.

- Max. Illumination of week light at 0.5m: ≥15000Lx

Max. Illumination of week light at 1m: ≥4500Lx

Max. Illumination of strong light at 0.5m: ≥125000Lx

Max. Illumination of strong light at 1m: ≥35000Lx

- Continuous working time of strong light: ≥70min

- Rated voltage: 16.8V   Battery capacity:  ≥5200mAh

- Weight: ≤1.6KG

- Overall dimension: ∅91*304mm(head ∅92mm，body ∅52mm, tail ∅60mm;  total length 304mm)

Main functions:

Function: The device has the long-range light function and dazzling function, can conduct the hard light and variable frequency blasting flash to the target person to make the person temporarily dizzy and blind.

Material: Metal resistance to high temperature luminous cup, good light focusing performance, Cree LED, aluminum alloy shell.

Water-proof: Good whole sealing performance, and the charging hole is enclosed.

Company profile

Hangzhou Hengli Electronic Technology Co., Ltd., established in 2002, is a professional manufacturer of lighting equipment for police and forensic light source, and it is a professional manufacturer integrating technology development, production and sales.

Since the foundation, the Company has developed ten series and more than ninety types professional lighting equipment and sources, including: forensic light source series, multi-band light source series, laser detection instrument, strong light search light series, strong light flashlight series, strong light working light series, (Portable light tower) lift-type strong light work light series, power-type lift working light series and forensic working light, etc.

Our company will has been committed to providing professional lighting, forensic light sources, laser light sources and crime scene investigation tools for public security departments of the government.

Add.: No.1 of Jianhua Area 2, GenShan East Road,Jianggan District, Hangzhou City, Zhejiang Province, China

Tel.: 0086-571-86987719     0086-571-86431402

Fax.: 0086-571-86431401

E-mail.: hzhl@lightmobile.com         Joyce

Website: www.lightmobile.com