Portable Infrared Light Source   OR-GIR90

Main Parameter:

- Wavelength: 850nm/940nm

- Power: 90W

- Battery Voltage: DC12.6V

- Battery Capacity: 5.6Ah

- Battery Type: Lithium-ion battery

- Charge current: DC12.6V 1A

- LED light source: composed of 18 LED spotlight cup.

- Switch mode:

- on/off(the button to start the self locking, and infrared minimum power opened)

- Up /Down(the buttons to adjust power respectively)

- Battery voltage test: when the voltage is saturated, the indicator light is green. When the voltage is the saturation state of 2/3, the indicate light is pink. Below 1/3 for the red light, and to remind the lack of electricity.

- Fixed mode: Hand held or fixed on the tripod 1/4＂interface(3/8＂can be converted to 1/4＂)

- Net weight: ≤1.8KG (including battery)

- Size: head: ≤Φ120mm    body: ≤Φ46mm    end: ≤Φ49mm    total length: ≤312mm

- Function: large light exposure area, distant light, with the use of infrared night vision.

- Application: applicable to the military, customs, border defense, public security Night reconnaissance and search for evidence.

Company profile

Hangzhou Hengli Electronic Technology Co., Ltd., established in 2002, is a professional manufacturer of lighting equipment for police and forensic light source, and it is a professional manufacturer integrating technology development, production and sales.

Since the foundation, the Company has developed ten series and more than ninety types professional lighting equipment and sources, including: forensic light source series, multi-band light source series, laser detection instrument, strong light search light series, strong light flashlight series, strong light working light series, (Portable light tower) lift-type strong light work light series, power-type lift working light series and forensic working light, etc.

Our company will has been committed to providing professional lighting, forensic light sources, laser light sources and crime scene investigation tools for public security departments of the government.

Add.: No.1 of Jianhua Area 2, GenShan East Road,Jianggan District, Hangzhou City, Zhejiang Province, China

Tel.: 0086-571-86987719     0086-571-86431402

Fax.: 0086-571-86431401

E-mail.: hzhl@lightmobile.com         Joyce

Website: www.lightmobile.com